## Slide 1
The Take-Away
Bending the integers 1 – 243, using clock arithmetic
Re-framing a special sequence of binary digits

## Slide 2
1. The Take-Away
This is the first in the series of teaching documents in the art of bending number.
There is a natural repetition of pattern in many objects surrounding us, in the context
of communication, ranging from the Honey Bee in Nature to the sequence of number
in the fabricated Internet traffic and even down to the electron orbital movement at
the Quantum Level.
It is due to the many facets of the plasticity in data manipulation of the measurements of the observations that allows for a beginner’s interpretation to evolve at all, and this introduction will demonstrate how one may look at data to spot the patterns,
however,
more importantly,
this series of teaching documents will also serve as an introduction to the understanding of the work horse of the work shown through this website; The Cepstrum; the underlying communication found within both the natural and the fabricated series of number from
measurement. The Cepstrum will be demonstrated to be a subtle and yet powerful tool.

## Slide 3
We start with the normal ordering of the first 243 integers:
1,2,3,4,5,6,7,…………………………………………………………………………………….243
Apply clock modulo arithmetic: with: a = 73, m = 243, ic= 1; then
for k = 1:m
s(k) = mod(a ic + 23,m);
ic = s(k);
end
To get the reordered sequence of 243 integers: From 1 to:
96, 227, 70, 30, 26, 220, 45, 149, 208, 141, 110, 34, 75, 152, 184, 90, 32, 172, 186, 236, 241, 120, 35,
148, 135, 158, 136, 231, 119, 205, 165, 161, 112, 180, 41, 100, 33, 2, 169, 210, 44, 76, 225, 167, 64,
78, 128, 133, 12, 170, 40, 27, 50, 28, 123, 11, 97, 57, 53, 4, 72, 176, 235, 168, 137, 61, 102, 179, 211,
117, 59, 199, 213, 20, 25, 147, 62, 175, 162, 185, 163, 15, 146, 232, 192, 188, 139, 207, 68, 127, 60, 29,
196, 237, 71, 103, 9, 194, 91, 105, 155, 160, 39, 197, 67, 54, 77, 55, 150, 38, 124, 84, 80, 31, 99, 203, 19
195, 164, 88, 129, 206, 238, 144, 86, 226, 240, 47, 52, 174, 89, 202, 189, 212, 190, 42, 173, 16, 219, 215,
166, 234, 95, 154, 87, 56, 223, 21, 98, 130, 36, 221, 118, 132, 182, 187, 66, 224, 94, 81, 104, 82, 177, 65,
151, 111, 107, 58, 126, 230, 46, 222, 191, 115, 156, 233, 22, 171, 113, 10, 24, 74, 79, 201, 116, 229, 216,
239, 217, 69, 200, 43, 3, 242, 193, 18, 122, 181, 114, 83, 7, 48, 125, 157, 63, 5, 145, 159, 209, 214, 93, 8,
121, 108, 131, 109, 204, 92, 178, 138, 134, 85, 153, 14, 73, 6, 218, 142, 183, 17, 49, 198, 140, 37, 51, 101,
106, 228, 143, 13, 0, 23, and then, back to 1.
Do you see the pattern? There is one, it’s a little wobbly, but there is a sub-pattern every 54 numbers.
Over the next few slides, we will bend this sequence into a very recognizable Spirograph pattern.
2. Bending the integers 1 – 243, using clock arithmetic

## Slide 4
First we plot the first five numbers of the ordered sequence: 1, 2, 3, 4, 5
So, we plot 1st goes to 1, 2nd goes to 2, 3rd goes to 3, 4th goes to 5, and 5th goes to 5.
And if we now plot all 243 numbers ordered in a row, we get this denser plot
This is called a stem
plot. It shows that
there are no more
points in between
to plot. This system
Is discrete as are all
Digitally sampled
Systems. Sometimes,
Patterns are lost when
The dots are connected.
9/10 I do not connect
the dots, however, 1/10
times I do.

## Slide 5
Now we plot the first five numbers of the clock-modulo sequence s : 1, 96, 227, 70, 30.
So, we plot 1st goes to 1, 2nd goes to 96, 3rd goes to 227, 4th goes to 70, and 5th goes to 30.
Now we plot all 243 numbers in the s sequence
Do you see the emerging pattern ?

## Slide 6
Plot from the previous slide
Now we take away the stems, and draw in ellipses to bring out some patterns

## Slide 7
Now we find some more
We have: 4 Blue ellipses, 5 green ellipses, and 2 red ellipses.
You know, we mentioned that the Cepstrum shows a strong component of 54.
Now this may be luck but:
243/54 = 4.5 exactly. And, 2*4.5 = 9 = 5 + 4. Not sure if this holds true other cases.
But, the ‘9’ is interesting.
Although we have formed some ellipses around the sequence to show patterns,
We will now BEND these numbers around a circle, and out pops the ‘9’

## Slide 8
Now suppose we wanted to connect
The number 1 to 2 then 2 to 3 then
3 to 4. It would like below.
Suppose we had a circle with 6 equally
spaced points, indicated in red and labeled
counter clockwise.
1
5
6
4
3
2
1
5
3
2
6
4
Note: yes it’s clock modulo arithmetic
which is clockwise, but our labeling
will follow a unit circle convention and
Go counter clockwise; And, we will place one
on the right center instead of the 1 o’clock position,
i.e. we are looking ahead to trigonometry

## Slide 9
1
5
6
4
3
2
Now suppose we wanted to connect 1 to 3 then 3 to 5 then 5 to 4 then 4 to 6 then 6 to 2 and finally 2 back to 1.
It would look like below.
So we bent the sequence 1,3,5,4,6,2,1 around the circle,
in segments.

## Slide 10
1
122
183
61
Now consider a circle of 243 points located on a circle. Rough
estimates of quarter points 61,122,and 183 are labeled for reference.
243

## Slide 11
Here we will connect the first nine points of s:
1 to 96 to 227 to 70 to 30 to 26 to 220 to 45 to 149
1
149
45
220
26
30
70
227
96

## Slide 12
Here we connected, in order, all the points around the circle using
the s sequence. Note the ‘9’ nodes of a ‘Spirograph’ design as we BEND
the sequence s around the circle, in segments.

## Slide 13
3. Re-framing a special sequence of binary digits
We start with a single digit ‘1’ as opposed to the 243 integers from clock modulo.
Now we will feed this single ‘1’ into a machine called a linear recursive sequencer which takes in the single one and puts out 1’s and 0’s.
Basically, we are studying a sequence of ON/OFF pulses taking place. This sequencing is used in a range of systems like photo-acoustics in medical imaging and cell phone communications.
Here is the algorithm:
N=1, S=[1 zeros(1,1000)];, D=[1 0 0 1 0 1],
states = zeros(max(length(N),length(D))-1,1);
window = 20; % Samples
for k = 1:iterations
[x,states] = filter(N,D,S((k-1)*window+1:k*window),states);
Ts = [ Ts, mod(x,2) ];
states = mod(states,2);
end
1 0 0 1 0 1 1 0 0 1 1 1 1 1 0 0 0 1 1 0 1 1 1 0 1 0 1 0 0 0 0 1 0 0 1 0 1 1 0 0 1 1 1 1 1 0 0 0 1 1 0 1 1 1 0 1 0 1 0 0 0 0 1 0 0 1 0 1 1 0 0 1 1 1 1 1 0 0 0 1 1 0 1 1 1 0 1 0 1 0 0 0 0 1 0 0 1 0 1 1
Here are the first 100 outputs:
Do you see the pattern? There is one, it’s not wobbly, it is straight up and repeats every 31 numbers. Over the next few slides, we will reframe this sequence into a matrix of rows and columns to make the pattern easy to see; this matrix formation is our main bending tool from now on

## Slide 14
1 0 0 1 0 1 1 0 0 1 1 1 1 1 0 0 0 1 1 0 1 1 1 0 1 0 1 0 0 0 0 1 0 0 1 0 1 1 0 0 1 1 1 1 1 0 0 0 1 1 0 1 1 1 0 1 0 1 0 0 0 0 1 0 0 1 0 1 1 0 0 1 1 1 1 1 0 0 0 1 1 0 1 1 1 0 1 0 1 0 0 0 0 1 0 0 1 0 1 1 (these last six start over)
Here is the 100 numbers again with contiguous sets of 31 numbers highlighted with color:
Here is a stem plot of the numbers, which shows allows us to see some repetition
Here is a stem plot of the numbers where groups of 31 are colored to highlight the repetition

## Slide 15
1 1 1
0 0 0
0 0 0
1 1 1
0 0 0
1 1 1
1 1 1
0 0 0
0 0 0
1 1 1
1 1 1
1 1 1
1 1 1
1 1 1
0 0 0
0 0 0
0 0 0
1 1 1
1 1 1
0 0 0
1 1 1
1 1 1
1 1 1
0 0 0
1 1 1
0 0 0
1 1 1
0 0 0
0 0 0
0 0 0
0 0 0
Here, the three contiguous sets of numbers
are written in 31 row x 3 column
matrix form.
And now, instead of
The symbols of
written numbers,
We will choose the
Color red to be a ‘1’
And the color blue
to be a ‘0’
The rows have labels
in increments of 5, but
There is a 31st row.
There are three
Columns.
A colorbar is placed
Alongside for reference.
Later on all the colors
On the colorbar will be
Used. Note: for now the
Yellow line is a marker
Between columns 1&2
And 2&3.
Is it easier to see
the pattern?
Conversion to
matrix

## Slide 16
This end the introduction to bending and reframing
Number to make patterns easier to identify.
In both cases we identified a number that told us where to bend:
With the clock modulo sequence example we used 54, and
with the linear recursive binary sequence we used 31.
We identified these number through what we called a Cepstrum or
a Cepstral coefficient. We will show how to obtain this coefficient later.
Our next topic will be on human and animal sounds, where we will
Listen to audio, plot the waveform, look for signs of a cepstral coefficient,
Use this coefficient to reframe the plot as a matrix and look for patterns.
Before we leave, here are two more patterns, which without the Cepstrum,
In my opinion, would be difficult to see.

## Slide 17
Lagniappe: A Linear Recursive Sequence from Group Theory
built for 63
A cepstrum picks out 63 with little effort

## Slide 18
Lagniappe: A Wasp Buzz natural at 136
544 samples at
22000 samples/sec
0.0247 seconds
One second
Wasp’s
Buzz
Four
Pieces
Of 136
Overlaid
In a moment, my friend George saw the pattern from the top plot, but he’s an old guy
I needed the Cepstrum